## Slide 1: Routing Essentials
Learning Outcomes:
  Routing Protocol Overview: How different routing protocols (Distance Vector, Enhanced Distance Vector, Link State and Path Vector) identify and advertise routes.
  Path Selection: Logic a router uses to identify the best route and install in it’s routing table.
  Static Routing: Fundamentals of static routing
  Virtual Routing and Forwarding: Creation of logical routers on a physical router.

## Slide 2: 1. Routing Protocol Overview
Routing protocols are used to learn routes to a non-attached network on a router.
Static Routing Protocols vs. Dynamic Routing Protocols.
  Static Routing Protocols: Does not update routes during topology changes. Design requirements or hardware limitations may force use of static routing.
  Dynamic Routing Protocols: Distributes routes between routers and updates routes without intervention during topology changes. Selects best loop free path.

## Slide 3: 1. Routing Protocol Overview
Dynamic Routing Protocols Types:
Distance Vector:
  Distance: Route metric(cost- hop count) to reach the destination network.
  Vector: Direction/interface to reach the network.
  Uses distance vector algorithms (Bellman Ford and Ford Fulkerson algorithms) to calculate best loop free paths.
  Modifies the received routes from neighbors.
  Does not have complete map of the whole topology.
  Require less memory and CPU.

## Slide 4: 1. Routing Protocol Overview
Dynamic Routing Protocols Types:
Enhanced Distance Vector:
  Diffusing Update Algorithm (DUAL) is an enhanced distance vector algorithm. In detail in EIGRP chapter.
  EIGRP (Enhanced Interior Gateway Routing Protocol) is a hybrid routing protocol that uses DUAL algorithm.
  Following are the enhancements:
    Rapid convergence times.
    Unlike distance vector algorithms, it only sends update when there is change in the network.
    Sends ‘hello’ and forms neighbor relationship like in link state protocols.
    Uses bandwidth, delay, load, reliability and MTU size as cost metrics.
    Has option of equal or unequal multipath load balancing.

## Slide 5: 1. Routing Protocol Overview
Dynamic Routing Protocols Types:
Link State Algorithms:
  Advertises the link state and metrics for all it’s connected links to directly connected routers and all other routers in the network.
  To populate link state routing table, each router then runs its own link state algorithms (Dijkstra SPF algo) to find best loop free path to every router on the network.
  OSPF is used primarily in enterprises and IS-IS used primarily in ISPs are 2 link state RPs.
  OSPF uses Link State Advertisements (LSAs) and IS-IS uses Link State Packets (LSPs) for advertisements.
Notes: RPs: Routing Protocols, OSPF : Open Shortest Path First, IS-IS : Intermediate Systems to Intermediate Systems.

## Slide 6: 1. Routing Protocol Overview
Dynamic Routing Protocols Types:
Path Vector Algorithms:
Similar to distance vector algorithm.
Uses Path Attributes (PAs) instead of distance (hop-count) to find best loop free paths.
BGP Path attributes (PAs) : AS_Path, multi-exit Discriminator (MED), origin, next hop, local preference, atomic aggregate and aggregator.
Advertises entire path for each destination.
Flexible policy: Each node can enforce it’s own policy to select best loop free path to the destination.
Notes: RPs: Routing Protocols, OSPF : Open Shortest Path First, IS-IS : Intermediate Systems to Intermediate Systems.

## Slide 7: 2. Path Selection
A router creates Forwarding Information Base (FIB) from Routing Information Base (RIB) or routing table.
A route in RIB with longest prefix length match for a packet is installed into FIB.
Router uses FIB to forward packets.
RIB is populated from various routing protocol processes in a router.
Path Selection Deciders:
  Prefix length
  Administrative Distance
  Metric
Notes: RPs: Routing Protocols, OSPF : Open Shortest Path First, IS-IS : Intermediate Systems to Intermediate Systems.