## Slide 1: IPv4 Subnetting
Learning Outcomes:
  Design Phase
  Implementation
  Analyze classful IPv4 networks
  Subnet Masks
  Analyze existing subnets
  Choosing subnet masks
  Variable Length Subnet Mask (VLSM)

## Slide 2: 1. Design Phase
Gather Requirements:
  Number of subnets required (X)
  Number of hosts/subnet required (Y)
  Decide whether one mask on all subnets(equal sized networks) or Variable Length Subnet Mask (Variable sized networks)
  IP network number that will be subnetted

## Slide 3: 1. Design Phase
Private IP address space :
Class of Networks | Private IP Networks | Number of Networks | Size (2H –2 ) | No. Network(N) & Host (H) bits
A | 10.0.0.0 | 1 | 224 –2 = 16,777,214 | N=8,H=24
B | 172.16.0.0 - 172.31.0.0 | 16 | 216 –2 = 65,534 | N=16,H=16
C | 192.168.0.0 - 192.168.255.0 | 256 | 28 –2 = 254 | N=24,H=8
For classful network subnetting with single mask for all subnets :
Total number of bits in 4 octets of IP address : 32
Number of network bits (N) : Can be 8,16 or 24
Number of host bits (H) : Can be 24, 16, 8
Number of subnets required from design requirement = X
Number of hosts/subnet required from design requirement = Y
Choose number of subnet bits (S), Such that 2s ≥ X
Choose number of host bits (H), where 2H -2 ≥ Y

## Slide 4: 1. Design Phase
Example Design:
  Class B network 172.16.0.0, 200 subnets and 200 hosts.
  Here, X = 200, Y = 200, S =? And H = ?
  We have, 2s ≥ 200 and 2H -2 ≥ 200
  Therefore, S ≥ log(2)/log(200) ≥ 7.64
  And H ≥ log(2)/log(202) ≥ 7.65
  Thus, S = 8 and H = 8
  Subnet IDs/addresses: 172.16.0.0,172.16.1.0,172.16.2.0, 172.16.3.0 and so on upto 172.16.254.0 and 172.16.255.0
  Each subnet has following network like structure: network ID/address 172.16.0.0 , broadcast ID/address 172.16.0.255, usable hosts range 172.16.0.1 through 172.16.0.254
Notes: Do further practice exercises from book.

## Slide 5: 2. Implementation
Implementation steps:
Assign range of subnets to locations such as: 172.16.0.0 through 172.16.127.0 to office in Asia that has 12 VLANs and rest subnets reserved for future expansion.
Similarly, 172.16.128.0 through 172.16.192.0 to Australia and remaining 172.16.193.0 through 172.16.255.0 to United States.
Assigning and reserving contiguous range of subnets to same geographic location helps in route summarization.
From each subnets assign lower range ip addresses as static for configuring network devices management ip and interface ip. Ex. 172.16.0.1 through 172.16.0.40
From each subnets assign remaining upper range ip addresses as DHCP to dynamically assign to end hosts through DHCP server. Ex. 172.16.0.41 through 172.16.0.254

## Slide 6: 3. Analyze Classful IPv4 Networks
IPv4 Classes:
The first octet value of IPv4 dictates the class of an address.
Classes | First octet value (leading bits) | Purpose
A | 1 - 126 (0) | Unicast large networks (ISPs)
B | 128 – 191 (10) | Unicast medium networks (Universities & large Enterprises)
C | 192 - 223 (110) | Unicast small networks(Home & Small businesses)
D | 224 – 239 (1110) | Multicast networks (224.0.0.5 used by OSPF)
E | 240 – 255 (1111) | Reserved for experimental and research purposes
In Class A adresses, network starting with 0 that is 0.0.0.0 is used for static routing and 127.0.0.0/8 for local device communication such as 127.0.0.1/8 as loopback address.

## Slide 7: 4. Subnet Masks
Continuous bits of 1's and 0's without interleaving 1's and 0's.
Subnet Masks Formats:
Binary for computer use: 11111111 00000000 00000000 00000000
Dotted decimal notation (DDN) for human readability: 255.0.0.0
Prefixes (CIDR) for human readability: /8
Converting between binary and prefix Masks:
Count number of 1's and write it in /P format and vice versa.
EX. 11111111 00000000 00000000 00000000 = \8
Ex. /16 = 11111111 11111111 00000000 00000000
Notes: Do converting between formats practice exercises from book.

## Slide 8: 4. Subnet Masks
Converting between binary and DDN Masks:
For each of 4 octets convert the binary value to decimal value and vice versa
EX. 11111111 00000000 00000000 00000000 = 255.0.0.0
Ex. 255.128.0.0 = 11111111 10000000 00000000 00000000
Each octet can have only one of the 9 values as shown in the table below.
Binary Mask Octet | Decimal Equivalent | Number of 1's
00000000 | 0 | 0
10000000 | 128 | 1
11000000 | 192 | 2
11100000 | 224 | 3
11110000 | 240 | 4
11111000 | 248 | 5
11111100 | 252 | 6
11111110 | 254 | 7
11111111 | 255 | 8

## Slide 9: 4. Subnet Masks
Converting between Prefix and DDN Masks:
Converting from prefix to DDN can be done by first writing number of 1's in each octet and then converting to decimal.
Ex. /19 = 11111111 11111111 11100000 00000000 = 255.255.224.0
Or it can be done by counting the number of 1's in the octet that has both 1's and 0's. Then use table in previous slide to find the decimal value in that octet.For octets with all 1's write 255 and octest with all 0's write 0.
Ex . /20 = 8 + 8 + 4 + 0 = 255.255.240.0
Notes: Do converting between formats practice exercises from book.

## Slide 10: 4. Classful and Classless Addressing
Classful Addressing:
This addressing scheme takes into consideration of classifying IPv4 addresses into class A,B and C.
It divides the 32 bits IPv4 address into three parts i.e Network part with N network bits, Subnet part with S subnet bits and host part with H host bits.
Classless Addressing:
This scheme does not take the IPv4 classes A,B and C into consideration.
Thus, this divides the 32 bits IPv4 addresses into two parts i.e Prefix with P bits and Host part with H bits.
Below picture shows the relationship between N,P,S and H
32 bits
Class A, N = 8; Class B, N = 16; and Class C, N =24
Notes: Practice exercises on page 353 chapter 15.

## Slide 11: 5. Analyzing existing subnets
Find Subnet ID/resident subnet/subnet number: Binary method
With an ip address /p prefix write in binary form P prefix bits and H host bits
Convert the ip address from DDN to binary
Copy the prefix bits and set host bits to zero (0) of the binary ip address
Convert the resulting binary ip address to DDN to get the subnet ID.
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  PPPPPPPPP PPPPPPPP PPHHHHHH HHHHHHHH
  10101100 00010000 10010110 00101001
  10101100 00010000 10000000 00000000
  172.16.128.0 = Subnet ID

## Slide 12: 5. Analyzing existing subnets
Find Broadcast address/Network broadcast: Binary method
With an ip address /p prefix write in binary form P prefix bits and H host bits
Convert the ip address from DDN to binary
Copy the prefix bits and set host bits to one (1) of the binary ip address
Convert the resulting binary ip address to DDN to get the broadcast address.
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  PPPPPPPPP PPPPPPPP PPHHHHHH HHHHHHHH
  10101100 00010000 10010110 00101001
  10101100 00010000 10111111 11111111
  172.16.191.255 = Broadcast address

## Slide 13: 5. Analyzing existing subnets
Find Subnet ID/resident subnet/subnet number: Shortcut method
Convert /p mask notation to DDN mask.
If any octet of the mask=255, copy the ip address
If any octet of the mask=0, write 0 in that octet of the resulting subnet ID.
If any octet is neither 255 nor 0, then convert that octet of ip address to binary, set host part to zero (0) and convert back to decimal.
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  255.255.192.0
  Copy octets 1 and 2 of the DDN ip address = 172.16
  Write zero (0) in fourth octet; 172.16. .0
  Octet 3 of mask = 192 (neither 255 nor 0), binary of 150 = 10010110, set host part to zero = 10000000, convert octet 3 to decimal =128.
  Thus, the subnet ID = 172.16.128.0
Notes: Complete practice exercises in page 365 and 369 of the chapter analyzing existing subnets.

## Slide 14: 5. Analyzing existing subnets
Find Broadcast address/Network broadcast: Shortcut method
Convert /p mask notation to DDN mask.
If any octet of the mask=255, copy the ip address
If any octet of the mask=0, write 255 in that octet of the resulting broadcast address.
If any octet is neither 255 nor 0, then convert that octet of ip address to binary, set host part to one (1) and convert back to decimal.
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  255.255.192.0
  Copy octets 1 and 2 of the DDN ip address = 172.16
  Write 255 in fourth octet; 172.16. .255
  Octet 3 of mask = 192 (neither 255 nor 0), binary of 150 = 10010110, set host part to 1 = 10111111, convert octet 3 to decimal =191.
  Thus, the broadcast address = 172.16.191.255
Notes: Complete practice exercises in page 365 and 369 of the chapter analyzing existing subnets.

## Slide 15: 5. Analyzing existing subnets
Find Subnet ID/resident subnet/subnet number: Difficult mask & predictability
Convert /p mask notation to DDN mask.
If any octet of the mask=255, copy the ip address
If any octet of the mask=0, write 0 in that octet of the resulting subnet ID.
If any octet is neither 255 nor 0, refer this octet as interesting octet. Calculate a magic number = 256 – mask. Set the octet to ip address that is multiple of this magic number without going over.
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  255.255.192.0
  Copy octets 1 and 2 of the DDN ip address = 172.16
  Write zero (0) in fourth octet; 172.16. .0
  Octet 3 of the mask = 192 (neither 255 nor 0), magic number = 256-192 = 64. Multiples of 64 = 0,64,128,192,256. Multiple of 64 that does not go over 150 Thus, the subnet ID = 172.16.128.0
Notes: Complete practice exercises in page 365 and 369 of the chapter analyzing existing subnets.

## Slide 16: 5. Analyzing existing subnets
Find Broadcast address/Network broadcast: Diffcult mask & predictability method
Convert /p mask notation to DDN mask.
If any octet of the mask=255, copy the ip address
If any octet of the mask=0, write 255 in that octet of the resulting broadcast address.
If any octet is neither 255 nor 0, refer this octet as interesting octet. Calculate a magic number = 256 – mask. Set the octet to ip address to (Subnet ID + magic number – 1)
Example 172.16.150.41/18, Here P = 18 and H = 32-18 = 14
  255.255.192.0
  Copy octets 1 and 2 of the DDN ip address = 172.16
  Write 255 in fourth octet; 172.16. .255
  Octet 3 of mask = 192, magic number = 256-192 = 64,
  third octet = 128 (subnet id from previous slide) + 64-1 = 191
  Thus, the broadcast address = 172.16.191.255
Notes: Complete practice exercises in page 365 and 369 of the chapter analyzing existing subnets.

## Slide 17: 6. Choosing subnet masks
General process of finding subnet masks:
Find the number of network bits (N) per class rule.
Calculate the minimum number of subnet bits(S) so that 2S ≥ number of subnets needed (X).
Calculate the minimum number of host bits (H) so that 2H - 2 = number of hosts/subnet needed (Y).
If N+S+H > 32, no mask meets the need.
If N+S+H = 32, one mask meets the need. Prefix /p = N+S
If N+S+H < 32, multiple masks meet the need.
  Calculate the value of prefix /p = N+S based on minimum value of S. Which maximizes the number of hosts/subnet.
  Calculate the value of prefix \p = 32 – H based on minimum value of H. Which maximizes the number of subnets.
  Complete range of masks include all prefixes between two prefixes calculated in above steps.
Example network 192.168.83.0 , X = 8 subnets and Y = 8 hosts/subnet:
  N = 24
  S = 3
  H = 4
  N+S+H = 24+3+4 = 31 < 32, step 6 applies.
  P = 24+3 = /27, P = 32-4 = /28
  Thus 255.255.255.224 and 255.255.255.240 masks can be used.
Notes: Complete practice exercises in page 513.

## Slide 18: 6. Choosing subnet masks
Finding all subnets with subnet bits (S) < 8:
Find the interesting octet in the DDN subnet mask. Which is the octet that is neither 255 nor 0.
Find the magic number = 256 - subnet mask's interesting octet value
Find the classful network number or the zero subnet of the ip address. The zero subnet has all subnet bits set to zero.
Find the consecutive subnet numbers:
  For uninteresting octets copy the previous subnet number's value.
  For interesting octet add the magic number to previous subnet number's value untill the value reaches 256.
Example Network 172.16.0.0, Mask 255.255.240.0
3rd octet is the interesting octet.
Magic number = 256-240 = 16
172.16.0.0
172.16.16.0, 172.16.32.0, 172.16.48.0, 172.16.64.0, 172.16.80.0, 172.16.96.0, 172.16.122.0 …..... 172.16.240.0
Notes: Complete practice exercises in page 513.

## Slide 19: 6. Choosing subnet masks
Finding all subnets with subnet bits (S) = 8:
With subnet bits (S) exactly equal to 8, only two cases occur:
  Class A network with mask 255.255.0.0, where entire second octet is subnet mask.
  Class B network with mask 255.255.255.0, where entire third octet is subnet mask.
For each case follow exactly same process as with less than 8 subnet bits.
Example 172.16.0.0, 255.255.255.0:
Here, 3rd octet is interesting octet.
Magic number = 256 – 255 =1
Thus, 172.16.0.0, 172.16.1.0, 172.16.3.0 …........
…... through to 172.16.255.0
Notes: Complete practice exercises in page 513.

## Slide 20: 6. Choosing subnet masks
Finding subnet IDs with subnet bits (S) > 8:
Process for 9 to 16 subnet bits, S = 9 to 16
  Calculate the subnet ID just as with 8 or less subnet bits. However, when it adds up to 256, move to the next step. Consider the subnet IDs calculated as subnet blocks.
  Copy the subnet blocks calculated in above steps but add 1 to the just-left-octet. Just-left-octet is the octet just left of the interesting octet.
  Repeat above steps until the just-left-octet reaches 255.
Example 130.4.0.0 255.255.255.192
  Since the network is class B network, N = 16, P = /26 and
  S = 26-16 = 10. Thus S > 8.
    Interesting octet = 4th octet. Magic number = 256 –192 = 64, subnet IDs will be: 130.4.0.0, 130.4.0.64, 130.4.0.128, 130.4.0.192 Here subnet blocks = 0,64,128,192
    Subnet IDs = 130.4.1.0, 130.4.1.64, 130.4.1.128, 130.4.1.192, 130.4.2.0, 130.4.2.64, 130.4.2.128 …....and so on until the third octet (just-left-octet) reaches 255. I.e, 130.4.255.0,130.4.255.64,130.4.255.128,130.4.255.192 and stop.
Notes: Complete practice exercises in page 523.

## Slide 21: 6. Choosing subnet masks
Finding subnet IDs with subnet bits (S) > 8:
Process for subnet bits, S ≥ 17. Since S ≥ 17, the subnet bits extend to 2nd and 3rd octet, and 4th octet is the interesting octet.
  Calculate the subnet ID just as with 8 or less subnet bits. However, when it adds up to 256, move to the next step. Consider the subnet IDs calculated as subnet blocks.
  Copy the subnet blocks calculated in above steps but add 1 to the 3rd octet.
  Repeat above steps until 3rd octet reaches 255.
  Add 1 to 2nd octet and repeat steps 2 & 3.
  Repeat step 4 until it reaches 255
Notes: Complete practice exercises in page 523.

## Slide 22: 6. Choosing subnet masks
Finding subnet IDs with subnet bits (S) > 8:
Example 10.0.0.0 255.255.255.192
  Since the network is class B network, N = 8, P = /26
  and S = 26-8 = 18. Thus S > 16.
Interesting octet = 4th octet. Magic number = 256 –192 = 64, subnet IDs will be: 10.0.0.0,10.0.0.64, 10.0.0.128, 10.0.0.192 Here subnet blocks = 0,64,128,192
Subnet IDs = 10.0.1.0, 10.0.1.64, 10.0.1.128, 10.0.1.192, 10.0.2.0, 10.0.2.64, 10.0.2.128, 10.0.2.192…....and so on
Repeat above until the third octet reaches 255. I.e, 10.0.255.0, 10.0.255.64, 10.0.255.128, 10.0.255.192
10.1.0.0,10.1.0.64,10.1.0.128,10.1.0.192,10.1.1.0,10.1.1.64,10.1.1.128,10.1.1.192 ….... so on until 10.1.255.0,10.1.255.64,10.1.255.128,10.1.255.192
10.2.0.0,10.2.0.64,10.2.0.128,10.2.0.192,10.2.1.0,10.2.1.64,10.2.1.128,10.2.1.192 ….... so on until 10.255.255.0,10.255.255.64,10.255.255.128,10.255.255.192
Notes: Complete practice exercises in page 523.

## Slide 23: 7. V LSM
Variable Length Subnet Mask (VLSM):
VLSM is using more than one subnet mask in a single classful network.
Example: 10.0.0.0/24 and 10.1.1.0/30 is VLSM
10.0.0.0/24 and 11.0.1.0/30 is not VLSM because they are in different class A network.
Finding VLSM Overlaps:
Find subnet ID and subnet broadcast address for each subnets of the internetwork.
For each subnets, check if any two subnets overlap.
Example network with ip address configured: Overlapping subnets are shown in red
IP addresses | Subnet ID | Broadcast address
10.1.34.9/22 | 10.1.32.0 | 10.1.35.255
10.1.29.101/23 | 10.1.28.0 | 10.1.29.255
10.1.23.254/22 | 10.1.20.0 | 10.1.23.255
10.1.17.1/21 | 10.1.16.0 | 10.1.23.255
10.1.1.1/20 | 10.1.0.0 | 10.1.15.255
Notes: Complete practice exercises in page 536.

## Slide 24: 7. V LSM
Adding new VLSM subnet:
Pick the subnet mask (prefix length) for the new subnet, based on the design requirements (if not already listed as part of the question).
Calculate all possible subnet numbers of the classful network using the mask from Step 1, along with the subnet broadcast addresses.
Make a list of existing subnet IDs and matching subnet broadcast addresses.
Compare the existing subnets to the candidate new subnets to rule out overlap-ping new subnets.
Choose the new subnet ID from the remaining subnets identified at Step 4,paying attention to whether the question asks for the numerically lowest or numerically highest subnet ID
Notes: Complete practice exercises in page 536.

## Slide 25: 7. V LSM
Adding new VLSM subnet: Example
Given subnets already in the internetwork
IP addresses | Subnet ID | Broadcast Address
172.16.2.1/23 | 172.16.2.0 | 172.16.3.255
172.16.9.1/30 | 172.16.9.0 | 172.16.9.3
172.16.9.5/30 | 172.16.9.4 | 172.16.9.7
172.16.4.1/23 | 172.16.4.0 | 172.16.5.255
172.16.6.1/24 | 172.16.6.0 | 172.16.6.255
New VLSM subnet requirements: network 172.16.0.0, use smallest possible subnet to accommodate 300 hosts/subnet. So, H = 9. P = /23. Below table lists some of the possible /23 subnets in 172.16.0.0
Subnet | Subnet Number | Broadcast Address
First (zero) | 172.16.0.0 | 172.16.1.255
Second | 172.16.2.0 | 172.16.3.255
Third | 172.16.4.0 | 172.16.5.255
Fourth | 172.16.6.0 | 172.16.7.255
Notes: First subnet (zero subnet) in second table does not overlap with any existing subnets in first table. Thus subnet 172.16.0.0/23 can be used. Or if zero subnet cannot be used, 172.16.10.0/23 does not overlap with existing subnets.
Complete practice exercises in Appendix H.