## Slide 1: Route Summarization
Learning Outcomes:
Foundation
Choosing Best Summary Routes

## Slide 2: 1. Foundation
Route Summarization need:
  Decreases the size of the routing table
  Longer routing tables consume more memory and takes up more CPU cycles for route lookups.
  Helps engineers with troubleshooting routing problems
  Decreases the number of routing protocol updates
  Helps with convergence of routing protocols

## Slide 3: 2. Choosing Best Summary Routes
Choosing the best summary routes:
  Works best if during subnetting, contiguous subnets are used in single router/location
  The word best, when applied to choosing what summary route to configure, means that the summary should include all the subordinate subnets, but with as few other addresses as is possible.
Example : subnets 10.3.4.0/24, 10.3.5.0/24,
10.3.6.0/24, and 10.3.7.0/24
Can be summarized with 10.3.0.0/16 which includes all the above subnets and many more.
Summarizing with 10.3.4.0/22, includes exactly above subnets only. Thus, this is best summary route.

## Slide 4: 2. Choosing Best Summary Routes
Choosing the best summary routes:
List all to-be-summarized (subordinate) subnet numbers in decimal, in order, from lowest to highest, along with their matching subnet broadcast addresses.
Note the low and high end of the range of addresses for all combined subnets by noting the numerically lowest subnet ID and numerically highest subnet broadcast address.
Pick a starting point prefix length /P for Step 4, as follows: Pick the shortest prefix length mask of all the subordinate subnets and then subtract 1.
Calculate a new potential summary subnet/mask, with matching broadcast address, based on the lowest subordinate subnet ID from the original list and the current prefix length.
    A. If the calculated range of addresses includes the entire range from Step 2, you have found the best summary route.
    B. If not, subtract 1 from the prefix length used in the most recent calculation and repeat Step 4.

## Slide 5: 2. Choosing Best Summary Routes
Choosing the best summary routes: Example
Routes:10.1.50.0/23,10.1.48.0/23,10.1.46.0/23,
10.1.52.0/23
Lowest subnet ID = 10.1.46.0/23, Highest subnet ID = 10.1.52.0/23
Highest broadcast address = 10.1.53.255
Lowest prefix = /23
New possible best summary route = 10.1.46.0/22
Check if it includes all the subordinate routes if not decrease prefix :
  Subnet ID = 10.1.44.0/22, subnet broadcast address = 10.1.47.255. Does not include all subordinate routes.
  New possible best summary route = 10.1.44.0/21
  Subnet ID = 10.1.40.0/21, subnet broadcast address = 10.1.47.255. Does not include all subordinate routes.
  New possible best summary route = 10.1.40.0/20
  Subnet ID = 10.1.32.0/20, subnet broadcast address = 10.1.47.255. Does not include all subordinate routes.
  New possible best summary route = 10.1.32.0/19
  Subnet ID = 10.1.32.0/19, subnet broadcast address = 10.1.63.255. Does include all subordinate routes.
Best summary route is 10.1.32.0/19
Notes: Practice exercises Appendix O.