## Slide 1: STATIC ROUTING
Learning Outcomes:
  Types of Static routing
  How they differ from one another
  Configuration Commands

## Slide 2: 1. Types of Static Routing
Directly Attached Static Routing
Recursive Static Routing
Multi-hop Topology Recursive Static Routing
Fully Specified Static Routing
Floating Static Routing
Null Static Routing

## Slide 3: 2. Description and Configuration Commands
Directly Attached Static Routing:
  A static route that uses only the outbound next-hop interface. Typically used in links with serial interfaces as they do not maintain adjacency tables and do not use ARP.Not recommended with ethernet links as it may cause system instability due to ARP lookup for each destination matching the route.
Recursive Static Routing:
  A recursive static route specifies the IP address of the next-hop address.
  Forwarding engine on Cisco devices needs to know which
  interface an outbound packet should use. Recursive
  lookup occurs when the router queries the RIB to locate
  the route toward the next-hop IP address (connected,
  static, or dynamic) and then cross-references the
  adjacency table.
ip route network subnet-mask next-hop-interface-id
ip route 10.1.17.0 255.255.255.0 Gi0/0
ip route network subnet-mask next-hop-ip
ip route 10.1.16.0 255.255.255.0 10.1.12.2

## Slide 4: 2. Description and Configuration Commands
Multi-hop Topology Recursive Static Routing:
  A recursive static route with multi-hop topology can specify the next-hop-ip of an interface that is multiple hop away. In such case, the router performs multiple recursive lookup when building the CEF entry for the destination network.
Fully Specified Static Routing:
  A static route with both the outbound interface and next-hop-ip address is called fully specified static route.
  If the outbound interface specified is not in up state, the router removes the static route from the RIB. Specifying the next-hop address and the physical interface removes the recursive lookup and does not involve the ARP processing problems while specifying only the outbound interface.
ip route network subnet-mask interface-id next-hop-ip
ip route 10.1.17.0 255.255.255.0 Gi0/0 10.1.12.1

## Slide 5: 2. Description and Configuration Commands
Floating Static Routing:
  The default AD on static routes is 1, but static routes can be configured with AD from 1 to 255 by appending the AD value to the command structure.
  Using a floating static route is common technique to provide a backup route to a route learned by dynamic routing protocol. A floating static route is configured with higher AD than the primary route. Because the AD is higher than the primary route the floating static route is only installed in RIB when the primary route is withdrawn.
Static Null Routing:
  Configuring a static route to Null/Virtual interface provides a method of dropping the traffic without configuring the Access Control List. The static route to a null interface uses a summarized network range and routes that are more specific points toward actual destination.
  Any packet with destination address in this range that does not have more specific routes will be routed to Null0 interface and will be dropped thus saving bandwidth and possible routing loops.
ip route 10.1.12.0 255.255.252.0 Null0
ip route 10.1.16.0 255.255.254.0 Null0
ip route network subnet-mask interface-id next-hop-ip AD
ip route 10.1.17.0 255.255.255.0 Gi0/0 10.1.12.1 210